ANNEX A - PROTOCOL IMPLEMENTATION CONFORMANCE STATEMENT (NORMATIVE)

(This annex is part of this Standard and is required for its use.)

BACnet Protocol Implementation Conformance Statement

Date: October 4, 2017____________________________

Vendor Name: Powers

Product Name: IntelliStation

Product Model Number: 109601

Application Software Version: _J1267H__  Firmware Revision: __406__  BACnet Protocol Revision: ______12______

Product Description:

The IntelliStation is a mixing control designed to deliver tempered water to plumbing fixtures. The control uses Proportional Integral (PI) logic to accurately maintain a target temperature by mixing a high temperature water source with a low temperature water source. ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

____________________________________________________________________________________________________

____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

BACnet Standardized Device Profile (Annex L):

( BACnet Operator Workstation (B-OWS)

( BACnet Advanced Operator Workstation (B-AWS)

( BACnet Operator Display (B-OD)

( BACnet Building Controller (B-BC)

( BACnet Advanced Application Controller (B-AAC)

( BACnet Application Specific Controller (B-ASC)

( BACnet Smart Sensor (B-SS)

( BACnet Smart Actuator (B-SA)

List all BACnet Interoperability Building Blocks Supported (Annex K): __

DS-RP-B

DS-RPM-B

DS-WP-B

DM-DDB-B

DM-DOB-B

DM-DCC-B____________________________________

____________________________________________________________________________________________________

Note: device communication control password is “Powers1017”.													_

Segmentation Capability:

( Able to transmit segmented messages	Window Size

( Able to receive segmented messages	Window Size

Standard Object Types Supported:

Device Object,

Analog Input: not creatable, not deletable

Analog Value: not creatable, not deletable

An object type is supported if it may be present in the device. For each standard Object Type supported provide the following data:

1) Whether objects of this type are dynamically creatable using the CreateObject service

2) Whether objects of this type are dynamically deletable using the DeleteObject service

3) List of the optional properties supported

4) List of all properties that are writable where not otherwise required by this standard

5) List of all properties that are conditionally writable where not otherwise required by this standard

6) List of proprietary properties and for each its property identifier, datatype, and meaning

7) List of any property range restrictions

Data Link Layer Options:

( BACnet IP, (Annex J)

( BACnet IP, (Annex J), Foreign Device

( ISO 8802-3, Ethernet (Clause 7)

( ATA 878.1, 2.5 Mb. ARCNET (Clause 8)

( ATA 878.1, EIA-485 ARCNET (Clause 8), baud rate(s) ____________

( MS/TP master (Clause 9), baud rate(s): 9600, 19200, 38400, 57600, 76800, 115200

( MS/TP slave (Clause 9), baud rate(s):

( Point-To-Point, EIA 232 (Clause 10), baud rate(s):

( Point-To-Point, modem, (Clause 10), baud rate(s):

( LonTalk, (Clause 11), medium: __________

( BACnet/ZigBee (ANNEX O)

( Other:

Device Address Binding:

Is static device binding supported? (This is currently necessary for two-way communication with MS/TP slaves and certain other devices.) ( Yes	( No

Networking Options:

( Router, Clause 6 - List all routing configurations, e.g., ARCNET-Ethernet, Ethernet-MS/TP, etc.

( Annex H, BACnet Tunneling Router over IP

( BACnet/IP Broadcast Management Device  (BBMD)

Does the BBMD support registrations by Foreign Devices?	( Yes	( No

Does the BBMD support network address translation?	( Yes	( No

Network Security Options:

( Non-secure Device - is capable of operating without BACnet Network Security

( Secure Device - is capable of using BACnet Network Security (NS-SD BIBB)

( Multiple Application-Specific Keys:

( Supports encryption (NS-ED BIBB)

( Key Server (NS-KS BIBB)

Character Sets Supported:

ANSI X.34

Indicating support for multiple character sets does not imply that they can all be supported simultaneously.

( ISO 10646 (UTF-8)	( IBM(/Microsoft( DBCS	( ISO 8859-1

( ISO 10646 (UCS-2)	( ISO 10646 (UCS-4)	( JIS X 0208

If this product is a communication gateway, describe the types of non-BACnet equipment/networks(s) that the gateway supports:

_______________________________________________________________________________________________

_______________________________________________________________________________________________

_______________________________________________________________________________________________