VH7200 Series

Protocol Implementation Conformance Statement (PICS)

Last revision: October 31st, 2011

Vendor Name:		Viconics

Product Name:		VH7200 Series

Product Model Number:		VH7200A1000B

VH7200D1000B

VH7270F1000B

VH7270D1000B

VH7270K1000B

Product Version:		4.0.05

BACnet Protocol Revision:		2 (135-2001)

###### Product Description

The VH7200 humidity controller family is specifically designed for control of humidification and dehumidification equipment such as steam header direct injection, desiccant wheel, or stand alone humidification / dehumidification equipment

BACnet Standardized Device Profile (Annex L):

( BACnet Operator Workstation (B-OWS)

( BACnet Building Controller (B-BC)

( BACnet Advanced Application Controller (B-AAC)

( BACnet Application Specific Controller (B-ASC)

( BACnet Smart Sensor (B-SS)

( BACnet Smart Actuator (B-SA)

BACnet Interoperability Building Blocks Supported (Annex K):

| BACnet Interoperability Building Block | Supported |
| --- | --- |
| Data Sharing-ReadProperty-B (DS-RP-B) | ( |
| Data Sharing-ReadPropertyMultiple-B (DS-RPM-B) | ( |
| Data Sharing-WriteProperty-B (DS-WP-B) | ( |
| Device Management-Dynamic Device Binding-B (DM-DDB-B) | ( |
| Device Management-Dynamic Object Binding-B (DM-DOB-B) | ( |
| Device Management-DeviceCommunicationControl-B (DM-DCC-B) | ( |

Segmentation Capability:

| Segmented Requests Supported | ( | Window Size: | N/A |
| --- | --- | --- | --- |
| Segmented Responses Supported | ( | Window Size: | N/A |

Standard Object Types Supported:

| Object Type | Supported | Dynamically Creatable | Dynamically Deletable | Optional Properties Supported | Writable Properties |
| --- | --- | --- | --- | --- | --- |
| Analog Input | ( | ( | ( | Reliability | Out_of_Service |
| Analog Value | ( | ( | ( | Reliability | Present_Valuea Out_of_Servicea |
| Binary Input | ( | ( | ( | Reliability Active_Text Inactive_Text | Out_of_Service |
| Binary Value | ( | ( | ( | Reliability Active_Text Inactive_Text | Present_Value Out_of_Service |
| Device | ( | ( | ( | Max_Master Max_Info_frames | Object_Identifier Object_name Max_Master |
| Group | ( | ( | ( | N/A | N/A |
| Multi-state Value | ( | ( | ( | Reliability States_Text | Present_Value Out_of_Service |

a : Present_Value and Out_of_Service properties are writable for every AV objects except :

- Room Humidity (AV14)

- Humidification Demand (AV17)

- Humidifier Output (AV22)

- Eff (Effective) Reset Humidification RH Spt (Setpoint) (AV29)

Data Link Layer Options:

( BACnet IP, (Annex J)

( BACnet IP, (Annex J), Foreign Device

( ISO 8802-3, Ethernet (Clause 7) (10Base2, 10Base5, 10BaseT, Fiber)

( ANSI/ATA 878.1, 2.5 Mb. ARCNET (Clause 8)

( ANSI/ATA 878.1, RS-485 ARCNET (Clause 8), baud rate(s):

( MS/TP master (Clause 9), baud rate(s): 9600, 19200, 38400, 76800 (Auto Baud)

( MS/TP slave (Clause 9), baud rate(s):

( Point-To-Point, EIA 232 (Clause 10), baud rate(s):

( Point-To-Point, modem, (Clause 10), baud rate(s):

( LonTalk, (Clause 11), medium:

( Other:

Device Address Binding:

Is static device binding supported? 		( Yes	( No

(Necessary for two-way communication with MS/TP slaves and certain other devices.)

Networking Options:

| Router | N/A |
| --- | --- |
| Annex H, BACnet Tunnelling | N/A |
| BACnet/IP Broadcast Management Device (BBMD) | N/A |
| Does the BBMD support registrations by Foreign Devices? | N/A |

Character Sets Supported:

| ( ANSI X3.4 | ( IBM/Microsoft DBCS | ( JIS C 6226 |
| --- | --- | --- |
| ( ISO 10646 (ICS-4) | ( ISO 10646 (UCS2) | ( ISO 8859-1 |

If this product is a communication gateway, describe the types of non-BACnet equipment/networks(s) that the gateway supports:

Not applicable.