VT7600 Series

Protocol Implementation Conformance Statement (PICS)

Last revision: October 31st, 2011

Vendor Name:		Viconics

Product Name:		VT7600 Series

Product Model Number:		VT7656B5x00B, VT7652B5x00B, VT7652H5x00B, VT7652A5x00B, VT7605B5x00B, VT7600H5x00B,

VT7600B5x00B, VT7600A5x00B.

VT7607B5x00B, VT7657B5x00B, VT7600W5x00B, VT7600F5x00B,

VT7606E5x00B, VT7652W5x00B.

VT7652F5x00B, VT7656E5x00B

Product Version:		3.5.07

BACnet Protocol Revision:		2 (135-2001)

###### Product Description

The VT7600 PI thermostat family is specifically designed for single stage and multi-stage control of heating/cooling equipment such as rooftop and self-contained units. The product features an intuitive, menu-driven, back-lit LCD display which walks users through the programming steps, making the process extremely simple. Accurate temperature control is achieved due to the product’s PI time proportional control algorithm, which virtually eliminates temperature offset associated with traditional, differential-based thermostats.

BACnet Standardized Device Profile (Annex L):

( BACnet Operator Workstation (B-OWS)

( BACnet Building Controller (B-BC)

( BACnet Advanced Application Controller (B-AAC)

( BACnet Application Specific Controller (B-ASC)

( BACnet Smart Sensor (B-SS)

( BACnet Smart Actuator (B-SA)

BACnet Interoperability Building Blocks Supported (Annex K):

| BACnet Interoperability Building Block | Supported |
| --- | --- |
| Data Sharing-ReadProperty-B (DS-RP-B) | ( |
| Data Sharing-ReadPropertyMultiple-B (DS-RPM-B) | ( |
| Data Sharing-WriteProperty-B (DS-WP-B) | ( |
| Device Management-Dynamic Device Binding-B (DM-DDB-B) | ( |
| Device Management-Dynamic Object Binding-B (DM-DOB-B) | ( |
| Device Management-DeviceCommunicationControl-B (DM-DCC-B) | ( |

Segmentation Capability:

| Segmented Requests Supported | ( | Window Size: | N/A |
| --- | --- | --- | --- |
| Segmented Responses Supported | ( | Window Size: | N/A |

Standard Object Types Supported:

| Object Type | Supported | Dynamically Creatable | Dynamically Deletable | Optional Properties Supported | Writable Properties |
| --- | --- | --- | --- | --- | --- |
| Analog Input | ( | ( | ( | Reliability | Out_of_Service |
| Analog Value | ( | ( | ( | Reliability | Present_Valuea Out_of_Servicea Object_Nameb |
| Binary Input | ( | ( | ( | Reliability Active_Text Inactive_Text | Out_of_Service |
| Binary Value | ( | ( | ( | Reliability Active_Text Inactive_Text | Present_Value Out_of_Service |
| Device | ( | ( | ( | Max_Master Max_Info_frames | Object_Identifier Object_Name Max_Master |
| Group | ( | ( | ( | N/A | N/A |
| Multi-state Value | ( | ( | ( | Reliability States_Text | Present_Value Out_of_Service |
| Schedule | ( | ( | ( | Weekly_schedule | Present_Value Weekly_Schedule |

a: Present_Value and Out_of_Service properties are writable for every AV object except :

- PI Heating Demand (AV20)

- PI Cooling Demand (AV21)

- Economizer Output (AV22)

- Analog Heat Output Status (AV35)

- Eff (Effective) Reset Humidification RH Spt (Setpoint) (AV96)

- Supply PI Heat Demand (AV97)

- Humidifier Output (AV101)

b: Present_Value and Out_of_Service properties are writable for every MV object except :

- Effective Occupancy (MV34)

c: Object_Name property is writable for the following objects only :

- Room_Temperature (AV7)

Data Link Layer Options:

( BACnet IP, (Annex J)

( BACnet IP, (Annex J), Foreign Device

( ISO 8802-3, Ethernet (Clause 7) (10Base2, 10Base5, 10BaseT, Fiber)

( ANSI/ATA 878.1, 2.5 Mb. ARCNET (Clause 8)

( ANSI/ATA 878.1, RS-485 ARCNET (Clause 8), baud rate(s):

( MS/TP master (Clause 9), baud rate(s): 9600, 19200, 38400, 76800 (Auto Baud)

( MS/TP slave (Clause 9), baud rate(s):

( Point-To-Point, EIA 232 (Clause 10), baud rate(s):

( Point-To-Point, modem, (Clause 10), baud rate(s):

( LonTalk, (Clause 11), medium:

( Other:

Device Address Binding:

Is static device binding supported? 		( Yes	( No

(Necessary for two-way communication with MS/TP slaves and certain other devices.)

Networking Options:

| Router | N/A |
| --- | --- |
| Annex H, BACnet Tunnelling | N/A |
| BACnet/IP Broadcast Management Device (BBMD) | N/A |
| Does the BBMD support registrations by Foreign Devices? | N/A |

Character Sets Supported:

| ( ANSI X3.4 | ( IBM/Microsoft DBCS | ( JIS C 6226 |
| --- | --- | --- |
| ( ISO 10646 (ICS-4) | ( ISO 10646 (UCS2) | ( ISO 8859-1 |

If this product is a communication gateway, describe the types of non-BACnet equipment/networks(s) that the gateway supports:

Not applicable.