VTR7300 Series

Protocol Implementation Conformance Statement (PICS)

Last revision: April 23rd, 2012

Vendor Name:		Viconics

Product Name:		VTR7300 Series

Product Model Number:		VTR7300A, VTR7305A,

VTR7350A, VTR7355A

Product Version:		2.5.07

BACnet Protocol Revision:		2 (135-2001)

###### Product Description

The VT7300 PI thermostat family is specifically designed for fan coil control. The product features a backlit LCD display with dedicated function menu buttons for simple operation. Accurate temperature control is achieved due to the product’s PI proportional control algorithm, which virtually eliminates temperature offset associated with traditional, differential-based thermostats.

Models are available for On/Off, 3 point floating and analog 0 to 10 Vdc control.

All models contain can control three, two or single fan speed. 3 additional inputs are also provided for various functions.

BACnet Standardized Device Profile (Annex L):

( BACnet Operator Workstation (B-OWS)

( BACnet Building Controller (B-BC)

( BACnet Advanced Application Controller (B-AAC)

( BACnet Application Specific Controller (B-ASC)

( BACnet Smart Sensor (B-SS)

( BACnet Smart Actuator (B-SA)

BACnet Interoperability Building Blocks Supported (Annex K):

| BACnet Interoperability Building Block | Supported |
| --- | --- |
| Data Sharing-ReadProperty-B (DS-RP-B) | ( |
| Data Sharing-ReadPropertyMultiple-B (DS-RPM-B) | ( |
| Data Sharing-WriteProperty-B (DS-WP-B) | ( |
| Device Management-Dynamic Device Binding-B (DM-DDB-B) | ( |
| Device Management-Dynamic Object Binding-B (DM-DOB-B) | ( |
| Device Management-DeviceCommunicationControl-B (DM-DCC-B) | ( |

Segmentation Capability:

| Segmented Requests Supported | ( | Window Size: | N/A |
| --- | --- | --- | --- |
| Segmented Responses Supported | ( | Window Size: | N/A |

Standard Object Types Supported:

| Object Type | Supported | Dynamically Creatable | Dynamically Deletable | Optional Properties Supported | Writable Properties |
| --- | --- | --- | --- | --- | --- |
| Analog Input | ( | ( | ( | Reliability | Out_of_Service |
| Analog Value | ( | ( | ( | Reliability | Present_Valuea, b Out_of_Servicea Object_Namec |
| Binary Input | ( | ( | ( | Reliability Active_Text Inactive_Text | Out_of_Service |
| Binary Value | ( | ( | ( | Reliability Active_Text Inactive_Text | Present_Value Out_of_Service |
| Device | ( | ( | ( | Max_Master Max_Info_frames | Object_Identifier Object_name Max_Master |
| Group | ( | ( | ( | N/A | N/A |
| Multi-state Value | ( | ( | ( | Reliability States_Text | Present_Valued Out_of_Serviced |

a : Present_Value and Out_of_Service properties are writable for every AV objects except :

- PI Heating Demand (AV21)

- PI Cooling Demand (AV22)

b : Present_Value property for Room Temperature (AV7) and Room Humidity (AV10) is writable only if Room Temp Override (BV8) is enabled and Room Humidity Override (BV11) is enabled respectively.

c : Object_Name property is writable for the following object only :

- Room Temperature (AV7)

d : Present_Value and Out_of_Service properties are writable for every MV objects except :

- Heating Valve Status (MV26)

- Cooling Valve Status (MV27)

- Fan Status (MV28)

Data Link Layer Options:

( BACnet IP, (Annex J)

( BACnet IP, (Annex J), Foreign Device

( ISO 8802-3, Ethernet (Clause 7) (10Base2, 10Base5, 10BaseT, Fiber)

( ANSI/ATA 878.1, 2.5 Mb. ARCNET (Clause 8)

( ANSI/ATA 878.1, RS-485 ARCNET (Clause 8), baud rate(s):

( MS/TP master (Clause 9), baud rate(s): 9600, 19200, 38400, 76800 (Auto Baud)

( MS/TP slave (Clause 9), baud rate(s):

( Point-To-Point, EIA 232 (Clause 10), baud rate(s):

( Point-To-Point, modem, (Clause 10), baud rate(s):

( LonTalk, (Clause 11), medium:

( Other:

Device Address Binding:

Is static device binding supported? 		( Yes	( No

(Necessary for two-way communication with MS/TP slaves and certain other devices.)

Networking Options:

| Router | N/A |
| --- | --- |
| Annex H, BACnet Tunnelling | N/A |
| BACnet/IP Broadcast Management Device (BBMD) | N/A |
| Does the BBMD support registrations by Foreign Devices? | N/A |

Character Sets Supported:

| ( ANSI X3.4 | ( IBM/Microsoft DBCS | ( JIS C 6226 |
| --- | --- | --- |
| ( ISO 10646 (ICS-4) | ( ISO 10646 (UCS2) | ( ISO 8859-1 |

If this product is a communication gateway, describe the types of non-BACnet equipment/networks(s) that the gateway supports:

Not applicable.