VZ7656X Series

Protocol Implementation Conformance Statement (PICS)

Last revision: July 5th, 2011

Vendor Name:		Viconics

Product Name:		VZ7656X Gen2 Zoning System Rooftop Thermostat

Product Model Number:		VZ7656R1000, VZ7656H1000, VZ7656F1000, VZ7656E1000

Product Version:		1.50.01

BACnet Protocol Revision:		4 (135-2004)

###### Product Description

The Viconics VZ7656X1000B thermostat series is specifically designed for RTU/HP/IAQ control of the Viconics Zoning System product family.

The RTU thermostat is designed for single stage or multi-stage control of heating/cooling equipment such as rooftop and self-contained units used in zoning systems.

The thermostats are used in conjunction with the Viconics VZ7260X5x00B Zone thermostats series for total system operation of each zones and the RTU.

BACnet Standardized Device Profile (Annex L):

( BACnet Operator Workstation (B-OWS)

( BACnet Building Controller (B-BC)

( BACnet Advanced Application Controller (B-AAC)

( BACnet Application Specific Controller (B-ASC)

( BACnet Smart Sensor (B-SS)

( BACnet Smart Actuator (B-SA)

BACnet Interoperability Building Blocks Supported (Annex K):

| BACnet Interoperability Building Block | Supported |
| --- | --- |
| Data Sharing COV-B (DS-COV-B) | ( |
| Data Sharing-ReadProperty-B (DS-RP-B) | ( |
| Data Sharing-ReadPropertyMultiple-B (DS-RPM-B) | ( |
| Data Sharing-WriteProperty-B (DS-WP-B) | ( |
| Device Management-Dynamic Device Binding-B (DM-DDB-B) | ( |
| Device Management-Dynamic Object Binding-B (DM-DOB-B) | ( |
| Device Management-DeviceCommunicationControl-B (DM-DCC-B) | ( |
| Device Management-TimeSynchronisation-B (DM-TS-B) | ( |
| Scheduling-Readonly-B (SCHED-R-B) | ( |

Segmentation Capability:

| Segmented Requests Supported | ( | Window Size: | N/A |
| --- | --- | --- | --- |
| Segmented Responses Supported | ( | Window Size: | N/A |

Standard Object Types Supported:

| Object Type | Supported | Dynamically Creatable | Dynamically Deletable | Optional Properties Supported | Writable Properties |
| --- | --- | --- | --- | --- | --- |
| Analog Input | ( | ( | ( | Reliability | Out_of_Service |
| Analog Value | ( | ( | ( | Reliability | Present_Valuea Out_of_Service |
| Binary Input | ( | ( | ( | Reliability Active_Text Inactive_Text | Out_of_Service |
| Binary Value | ( | ( | ( | Reliability Active_Text Inactive_Text | Present_Valueb Out_of_Service |
| Device | ( | ( | ( | Max_Master Max_Info_frames | Object_Identifier Object_name Max_Master |
| Multi-state Value | ( | ( | ( | Reliability States_Text | Present_Valuec Out_of_Service |
| Schedule | ( | ( | ( | Weekly_schedule | Read Only |

a: Present_Value property is writable for every AV objects except :

- Cfg RTC MAC (AV1)

- GUI Current Zone PI Heat Demand (AV11)

- GUI Current Zone PI Cool Demand (AV12)

- GUI Transferred PI Heat Demand (AV13)

- GUI Transferred PI Cool Demand (AV14)

- GUI Highest PI Heat Zone (AV15)

- GUI Highest PI Cool Zone (AV16)

- GUI Highest PI Heat Demand (AV17)

- GUI Highest PI Cool Demand (AV18)

- Cfg Device Instance (AV21)

- GUI Supply PI Heat Demand (AV28)

- GUI Fresh Air Level (AV39)

- GUI CO2 Level (AV40)

- GUI Highest CO2 Zone (AV41)

- GUI Economizer Output (AV42)

b: Present_Value and Out_of_Service properties are writable for every BV objects except :

- Sta Comm Lost Status (BV3)

- Sta Smart Reccovery (BV7)

- Sta Supply Heat Lockout Status (BV12)

c: Present_Value and Out_of_Service properties are writable for every MV objects except :

- Cfg RTC Baud (MV1)

- GUI Zone Sequence (MV4)

Data Link Layer Options:

( BACnet IP, (Annex J)

( BACnet IP, (Annex J), Foreign Device

( ISO 8802-3, Ethernet (Clause 7) (10Base2, 10Base5, 10BaseT, Fiber)

( ANSI/ATA 878.1, 2.5 Mb. ARCNET (Clause 8)

( ANSI/ATA 878.1, RS-485 ARCNET (Clause 8), baud rate(s):

( MS/TP master (Clause 9), baud rate(s): 9600, 19200, 38400, 76800 (Auto Baud)

( MS/TP slave (Clause 9), baud rate(s):

( Point-To-Point, EIA 232 (Clause 10), baud rate(s):

( Point-To-Point, modem, (Clause 10), baud rate(s):

( LonTalk, (Clause 11), medium:

( Other:

Device Address Binding:

Is static device binding supported? 		( Yes	( No

(Necessary for two-way communication with MS/TP slaves and certain other devices.)

Networking Options:

| Router | N/A |
| --- | --- |
| Annex H, BACnet Tunnelling | N/A |
| BACnet/IP Broadcast Management Device (BBMD) | N/A |
| Does the BBMD support registrations by Foreign Devices? | N/A |

Character Sets Supported:

| ( ANSI X3.4 | ( IBM/Microsoft DBCS | ( JIS C 6226 |
| --- | --- | --- |
| ( ISO 10646 (ICS-4) | ( ISO 10646 (UCS2) | ( ISO 8859-1 |

If this product is a communication gateway, describe the types of non-BACnet equipment/networks(s) that the gateway supports:

Not applicable.